## Slide 1: Sockets Programming
The lessons covered in this module are:
Connection Oriented
Concurrent and Iterative Server

## Slide 2: Socket
A socket is used to communicate between different machines (different
IP addresses). Socket of type SOCK_STREAM is full-duplex byte
streams.
Socket Program
Server
Client

## Slide 3: TCP / IP Protocol Stack
APPLICATION
(telnet / ftp )
TCP
Device driver
&
Hardware
IP
Sockets
User process
Kernel
Communication
details
Application
details
UDP

## Slide 4: Concurrent Server
Concurrent Server
Socket Program
Server
Client x
Client 1
Client y

## Slide 5: Socket : Definition
A socket is a communication endpoint and represents abstract object that a process may use to send or receive messages.
The socket frame work is procedural not message based
The two most prevalent communication APIs for Unix Systems are Berkeley Sockets and System V Transport Layer Interface(TLI)

## Slide 6: Sockets in Unix
The typical client -server relationship is not symmetrical
Network Connection can be connection-oriented or connectionless
More parameters must be specified for network connection, than for file I/O
The Unix I/O system is stream oriented
The network interface should support multiple communication protocol
Notes: Not symmetrical: To start a network connection, the application program should know which role it is going to play, server or client.
Connection oriented: TCP, SOCK_STREAM. Two way connected communication streams. Ex: telnet, HTTP
Connectionless: UDP (User Datagram Protocol) , SOCK_DGRAM. Build a packet, write an IP header on it with destination information, and send it out. It is generally used for packet by packet transfers of information. Ex: tftp, bootp, etc.
For a file: we need to pass: file descriptor, address and size of a buffer in a read or write system call.
For a socket: we need to pass a protocol, server IP address, port number, client IP address and size of client structure address.

## Slide 7: Socket Functions
connect( )
write( )
read( )
close( )
socket( )
close( )
read( )
write( )
read( )
accept( )
listen( )
bind( )
socket( )
Connection establishment
3 way hand shake
request
reply
End of file notification
TCP Server
Blocks until connection from client
TCP Client
Notes: This figure explains a three –way-handshake of connection-oriented socket.
First server creates a sock descriptor using socket system call, this is called a raw socket descriptor. Then it assigns IP address and port number and binds to them. The listen system call is having information about backlog queue number. Finally the accept system call is waiting for a client request.
In the client side, the client creates a socket descriptor and connects to the server. If the connection is successful client can write to the server. Then server reads the information from the client and writes back to the client. The client reads the information from the server and closes the connection. The server on being notified that the client has closed the connection, closes the client connection and waits for the next client request.

## Slide 8: socket system call
int socket (int domain,int type,int protocol);
Domain
  AF_UNIX for UNIX domain
  AF_INET for Internet domain
Socket type
  SOCK_STREAM for TCP (Connection Oriented)
  SOCK_DGRAM for UDP (Connectionless)
Protocol
  Protocol number is used to identify an application. List of the protocol number and the corresponding applications can be seen at /etc/protocols.
The socket system call returns a socket descriptor on success and -1 for failure.

## Slide 9: sockaddr_in structure
struct sockaddr_in {
short int sin_family;
unsigned short int sin_port;
struct in_addr sin_addr;
};
sin_family - address family
sin_port - port number
sin_addr - internet address (IP addr)
The in_addr structure used to define sin_addr is as under
struct in_addr {
unsigned long s_addr; /* refers to the four byte IP address */
}

## Slide 10: Byte Ordering ex: 91, 329 hex: 00 01 64 C1
High order byte low order byte
Little endian byte order : Ex: Intel series
Increasing memory address
Address A+1
Address A
Big endian byte order : ex: IBM 370, Motorola
High order byte low order byte
Increasing memory address
Address A+1
Address A
00 01 64 C1
C1 64 01 00

## Slide 11: Byte Ordering Functions
Internet protocols use big endian byte ordering called network byte order
The following functions allow conversions between the formats.
#include <netinet/in.h>
htons() – "Host to Network Short"
htonl() – "Host to Network Long"
ntohs() – "Network to Host Short"
ntohl() – "Network to Host Long"
h stands for host n stands for network
s stands for short l stands for long

## Slide 12: bind ( )
int bind(int sockfd, struct sockaddr *my_addr,int addrlen);
sockfd - the socket file descriptor returned by socket().
my_addr - a pointer to a struct sockaddr that contains information about IP address and port number.
addrlen - set to sizeof (struct sockaddr)
Notes: bind function assigns a IP address and port no to a socket.
Servers need to publish their address at which the clients have to contact them. So servers bind their well -known port when they start.
Normally TCP clients do not bind an address to its socket. The kernel chooses the address when the socket is connected.
A common error that occurs when bind is called is EADDRINUSE (“Address already in use”), which happens when some other socket is already using this port.

## Slide 13: connect ( )
int connect (int sockfd, struct sockaddr *serv_addr, int addrlen);
sockfd - the socket file descriptor returned by socket().
serv_addr - is a struct sockaddr containing the destination port and IP address.
addrlen - set to sizeof (struct sockaddr).

## Slide 14: listen ( )
int listen (int sockfd,int backlog);
sockfd - the socket file descriptor returned by socket().
backlog - the number of connections allowed on the incoming queue.
Backlog should never be zero as servers always expect connection from client.
The listen function converts an unconnected socket into a passive socket.
On successful execution of listen is indicating that the kernel should accept incoming connection requests directed to this socket.

## Slide 15: accept ( )
int accept (int sockfd, void *addr, int *addrlen);
sockfd
  the socket file descriptor returned by socket().
addr
  a pointer to a struct sockaddr_in. The information about the incoming connection like IP address and port number are stored.
addrlen
  a local integer variable that should be set to sizeof (struct sockaddr_in) before its address is passed to accept().
Notes: On successful accept, the system call returns with a new file descriptor, which refers to the TCP connection with the client.
Accept returns with the next completed connection queue. If this queue is empty, then the process is put to the sleep state.
It also returns with the client information like protocol, ip address etc.,
The connected socket is closed each time when the client closes the connection but the listening socket remains open for the lifetime of the server.

## Slide 16: close ( )
Socket descriptor can be closed like file descriptor.
close (sockfd);
Close system call prevents any more reads and writes to the socket. For attempting to read or write the socket on the remote end will receive an error.

## Slide 17: shutdown ( )
int shutdown (int sockfd, int how);
sockfd - socket file descriptor of the socket to be shutdown.
how – if it is
  0 - Further receives are disallowed
  1 - Further sends are disallowed
  2 - Further sends and receives are disallowed.
The shutdown system call gives more control (than close (sockfd) over how the socket descriptor can be closed.

## Slide 18: Pseudo Code
Server | Client
struct sockaddr_in serv, cli; sd = socket (AF_INET, SOCK_STREAM, 0); serv.sin_family = AF_INET; serv.sin_addr.s_addr = INADDR_ANY; serv.sin_port = htons (portno); bind (sd, &serv, sizeof (serv)); listen (sd, 5); nsd = accept (sd, &cli, &sizeof (cli)); read / write (nsd, ….); | struct sockaddr_in serv; sd = socket (AF_INET, SOCK_STREM, 0); serv.sin_family = AF_INET; serv.sin_addr.s_addr = inet_addr (“ser ip”); serv.sin_port = htons (portno); connect (sd, &server, sizeof (server)); read / write (sd, ….);

## Slide 19: Iterative Server
One client request at a time.
nsd = accept (sd, &cli,…);
while (1) {
read/write(nsd, …);
}

## Slide 20: Concurrent Server
Many clients requests can be serviced concurrently
while (1) {
nsd =(accept (sd, &cli, ….);
if (!fork( )) {
close(sd);
read/write(nsd, …..);
exit();
} else
close(nsd);
}