## Slide 1
Copyright 2003 - ATR Labs - All Rights Reserved.
Subject :
Memory Architecture - 2

## Slide 2
Types of “Addresses”
Logical Address : Specified by the binary code of the program. Generated by the compiler->linker->loader. Each logical address consists of a “segment” and an “offset”.
Linear Address : Also known as a “Virtual Address” Linear addresses range from 0 to the maximum addressability of the processor . For a 32-bit computer, the linear address could range from 0x0000-0000 to 0xFFFF-FFFF ( 4 GB ). The Pentium Pro ( first in the P6 family of processors ) has a Physical Address of 36 bits to accommodate 64 GB Physical RAM, but can still generate only 32-bit Linear Addresses. This is possible using a mechanism known as PAE ( Physical Address Extension Paging Mechanism ).
Physical Address : The address sent by the CPU to the RAM on the memory bus. Used to address memory cells in memory chips.
Logical Address
Linear Address
Physical Address
Segmentation
Unit
Paging
Unit
Logical Address Translation

## Slide 3
Review - Real Mode Addressing
The 8088 and the 8086 operate in Real Mode only.
From the 80286 onwards, all processors operate in both the real as well as protected mode.
Real Mode operation allows the processor to address only the first 1 MB of memory space, even for the Pentium or P4 processors.
Operating Systems like MSDOS and PCDOS assume that the processor operates only in Real Mode at all times, including when running on the Pentium or P4.
Real Mode operation allows application software written for the 8086/8088 which contain only 1 MB of memory to function in the 80286 and above without changing software.
In all cases, each of the Intel family of microprocessors begins operations in the real mode by default on powering-on or when the microprocessor is reset.
A combination of a segment register and an offset address access a memory location in the real mode. All addresses generated by a program consist of a segment and an offset.
The segment address located within one of the segment registers ( CS, DS, SS, ES ) defines the beginning address of any 64-K byte memory segment. The offset component selects any location within the 64-K byte segment.

## Slide 4
64 K-byte
Segment
00000
10000
1F000
1FFFF
FFFFF
1000
Segment Register
Offset = F000
The segment register is appended with 0h at its rightmost end. This effectively multiplies it by 16 to make it into a 20-bit address ( left shifted by 4 bits ).
All segments start on a paragraph boundary, i.e two consecutive segments will be separated by 16-bytes.
Segment Register = 1000 points to start of memory location 10000.
Segment Register = 1001 points to start of memory location 10010. Thdifference = 10h which is equal to 16 bytes.
In Real Mode, once the beginning address is known, the ending address of the segment is automatically ascertained by adding 64 KB ( the offset value ).
The segment and offset address is often written as xxxx:yyyy which means a physical address of xxxx0 + yyyy ( all in hexa ).
Real Mode Addressing....

## Slide 5
Default Register Combinations
Default Segment & Offset Registers:
The microprocessor has a set of rules whenever memory is addressed whether in the Real Mode or in the Protected Mode.
These define the Segment/Offset combinations used by certain addressing modes.
For example the Code Segment is always used with the IP to address the next instruction.This combination is CS:IP or CS:EIP depending on the mode of operation.
Segment Offset Special Purpose
CS IP Instruction Address SS SP or BP Stack Address DS BX, DI, SI, Data Address an 8-bit number or a 16-bit number ES DI for string instrns. String Destination Address
Segment Offset Special Purpose
CS EIP Instruction Address SS ESP and EBP Stack Address DS EAX, EBX, ECX, EDX, Data address ESI, EDI,an 8-bit number or a 32-bit number ES DI for string instrns. String Destination Address
8086-80486/Pentium default 16-bit segment and offset address combinations
80386-80486/Pentium default 32-bit segment and offset address combinations

## Slide 6
Protected Mode Addressing
Allows access to data and programs located above the first 1M byte of memory.
In place of the segment address, the segment register contains a selector that selects a descriptor from a descriptor table. The descriptor describes the memory segment's location, length and access rights.
Because the segment + offset register still access memory, protected mode instructions are identical to real mode instructions. In fact most programs writen to function in the real mode will function without change in the protected mode. The difference between modes is in the way the segment register is interpreted by the microprocessor to access the memory segment.
gdt or ldt (each containing 8192 entries)
Index - 13 bits
TI
x
+
gdtr / ldtr (contains the
physical address of start of
the table in memory )
Descriptor
+
Offset
Linear Address
Segment Register
Table Indicator
8

## Slide 7
IA-32 System Level Registers and Data Structures

## Slide 8
Selectors and Descriptors
The selector, located in the segment register, selects one of 8192 descriptors from one of two tables of descriptors.
The descriptor describes the location, length and access rights of the segment of memory.
There are two descriptor tables used with segment registers. One contains global descriptors and the other contains local descriptors. (The address of gdt is stored in gdtr, and current ldt is in ldtr).
The global descriptors contain segment definitions that apply to all programs, while the local descriptors are usually unique to an application.
Each descriptor table contains 8,192 descriptors, so a total of 16,384 descriptors are available to an application at any time. Because the descriptor describes a memory segment, this allows upto 16,384 segments to be described for each application.
Each descriptor is 8 bytes so the GDT and LDT are each a maximum of 64 KBytes in length.
Descriptors for the 80286 differ from the 386-to-Pentium but is upward compatible
0 0 0 0 0 0 0 0
0 0 0 0 0 0 0 0
Access Rights
Base(B23-B16)
Base (B15-B0)
Limit (L15-L0)
Base(B31-B24)
Access Rights
Base(B23-B16)
Base (B15-B0)
Limit (L15-L0)
G
D
O
AV
Limit L19-L16
80286-descriptor
80386/486/Pentium-descriptor
Format of a descriptor

## Slide 9
Details of the descriptor
The base address of the descriptor describes the starting location of the memory segment.
For the 80286 the base address is a 24-bit address so segments begin at any location within its 16MBytes of memory. Note that the paragraph boundary limitation is removed when operating in the protected mode.
The 80386 and above use a 32-bit base address that allows a segment to begin at any location in its 4GB of memory. Note how the 286 is upward compatible with the 386 because its most significant 8-bits are 00H.
The segment limit contains the last offset address found in a segment.
For example, if a segment begins at memory location F00000H and ends at location F000FFH the base address is F00000H and the limit is FFH. For the 286 processor the base address is F00000H and the limit is 00FFH and for the 386 and above the base address is 00F00000H and the limit is 000FFH.
Notice that the 286 has a 16-bit limit and the 386 and above have a 20-bit limit.
This means that the 286 accesses memory segments that are between 1 to 64 KBytes in length whereas the 386 and above access memory segments that are between 1 and 1 MByte in length (or 4K and 4GB in length --> see Granularity Bit in next slide ).

## Slide 10
Descriptors... contd.
There is another feature found in the 386 and above descriptor that is NOT in the 286. This is the Granularity Bit. If G = 0, then the limit specifies a segment limit of 1 to 1MB in length. If the Granularity Bit = 1, then the value of the limit is multiplied by 4K bytes ( appended with 000H ).
If G=1 the limit is any multiple of 4K bytes.
The reason that the segment length is 64 K Bytes in the 286 is that the offset address is always 16-bits because of its 16-bit internal architecture. The 386 and above use a 32-bit architecture which allows an offset address, in the protected mode of 32 bits. This 32-bit offset allows segment lengths of 4G Bytes.
The AV bit is used by some O.S'es to indicate availability ( ignored by Linux ).
The D-Bit indicates how the 386 and above instructions access register and memory data in the protected or real mode. ( If D = 0, the instructions are 16-bit instructions compatible with the 8086-80286 microprocessors. If D = 1 then the instructions are 32-bit instructions.
The Access Rights Byte ( ARB) controls access to the protected mode memory segment. This byte describes how the segment functions in the system. The ARB allows complete control over the segment.
If the segment is a data segment, the direction of growth is specified ( upwards for Data and downwards for Stack).If a segment grows beyond its limit, the program is interrupted indicating a GPF or General Protection Fault. You can even specify if a data segment can be written or is write protected. The code segment is also controlled in a similar fashion and can have reading inhibited to protect software.

## Slide 11
The Access Rights Byte
P
DPL
S
E
ED/C
R/W
A
A=0 segment not accessed A=1 segment has been accessed
E=0 Descriptor describes a data segment ED=0 Segment expands upward (data segment) ED=1 Segment expands downward(stack segm.) W=0 Data may not be written W=1 Data may be written E=1 Descriptor describes code segment C=0 Ignore Descriptor Privilege Level C=1 Abide by privilege level R=0 Code segment may not be read R=1 Code segment may be read.
S=0 System Descriptor S=1 Code or Data segment descriptor
DPL= The Descriptor Privilege Level
P = 0 The Descriptor is undefined P = 1 Segment contains a valid base and limit

## Slide 12
Functioning of the segment register in protected mode
Selector
TI
RPL
0
1
2
3
15
Requested Privilege Level where 00 is the highest and 11 is the lowest. Linux uses only levels 0 and 3 which are called “Kernel Mode” and “User Mode”
Table Indicator
TI = 0 Global Descriptor Table TI = 1 Local Descriptor Table
Selects one descriptor from 8,192 descriptors in either the global or the local descriptor table.
Note that bits 3 to 15 mean 13 bits. 213 = 8,192
Note that if the RPL matches or exceeds the priority that has been set by the access rights byte then access is granted. For example if the RPL is 10 and the ARB sets the segment privilege level as 11 access is granted.

## Slide 13
Program Invisible Registers
The global and local descriptor tables are found in the memory system. In order to access and specify the address of these tables, the 80386 and above contain program-invisible registers.
The program invisible registers are not directly addressed by software, so they are given this name although some of these registers are accessed by the system software.
Base Address
Base Address
Limit
Access
Access
Limit
Base Address
Limit
Segment Registers
Descriptor Cache
CS
GS
FS
SS
ES
DS
TR
LDTR
GDTR
IDTR
Program Invisible
Descriptor Table Addresses

## Slide 14
Program Invisible Registers...Contd.
Each of the segment registers contains a program-invisible portion used in the protected mode.
The program invisible portion of these registers is often called cache memory but this is NOT to be confused with the Level 1 or Level 2 caches found in the microprocessor.
The program invisible portion of the segment register is loaded with the base address, limit and access rights each time the number in the segment register is changed.
It is held there and used to access the memory segment until the segment number is changed again. This allows the microprocessor to access a memory segment repeatedly without referring back to the descriptor table for each access, hence the term cache.
Note:
1. The 80286 does not contain FS and GS nor the program invisible portions of these registers. 2. The 80286 contains a base address that is 24 bits and a limit that is 16 bits 3. The 80386/486/Pentium contain a base address that is 32 bits and a limit that is 20 bits 4. The access rights are 8 bits in the 286 and 12-bits in the 386 and above.
The GDTR (Global Descriptor Table Register) and IDTR(Interrupt Descriptor Table Register) contain the base address of the descriptor table and its limit. The limit of each descriptor table is 16-bits because the maximum table length is 64K bytes. The location of the local descriptor table is selected from the global descriptor table. One of the global descriptors is set up to address the local descriptor table.

## Slide 15
Program Invisible Registers...Contd.
The Task Register ( TR) holds a selector that accesses a descriptor that defines atask. A task is most often a procedure or application program. The descriptor for the procedure or application program is stored in the global descriptor table, so access can be controlled through the privilege levels.
The task register allows a context switch in about 17 µs ( microseconds) which is a fairly short amount of time. The task switch allows multitasking systems to switch from one task to another in a simple and orderly fashion.

## Slide 16
Memory Paging
The memory paging mechanism located within the 386 and above allows any physical memory location to be assigned to any linear address.
The linear address is defined as the address generated by the program. With the memory paging unit, the linear address is invisibly translated into any physical address. This allows an application written to function at a specific address to be relocated through the paging mechanism. It also allows memory to be placed into areas where no memory exists. An example is the upper memory blocks provided by EMM386.EXE.
The EMM386.EXE program reassigns extended memory in 4K blocks to the system memory between the video BIOS and the system BIOS ROMS to provide upper memory blocks. Without the paging mechanism, the use of this area of memory is impossible.

## Slide 17
Paging Registers
Page Directory Base Address
Page Fault Linear Address
Reserved
PG
CR0
CR1
CR2
CR3
0
31
11
12
The registers important to paging unit are CR0 and CR3. The leftmost bit PG of CR0 selects paging when placed at logic level 1. If the PG bit is cleared to 0 the linear address generated by the program becomes the physical address used to access memory.
CR3 contains the page directory base address and the PCD (Page Cache Disable) and PWT (Page Write Through) bits. The PCD and PWT bits control the operation of the PCD and PWT pins on the processor. If PCD is set (1), The PCD pin becomes a logic 1 during bus cycles that are not pages. This allows the external hardware to control the Level 2 cache memory. The L2 cache is an external high-speed memory that acts as a buffer between the processor and the main DRAM. The PWT bit also appears on the PWT pin during bus cycles that are not pages to control the write through cache in the system.
The Control Register Structure of the processor
PCD
PWT

## Slide 18
Paging Registers... Continued.
Page Directory Base Address
Page Fault Linear Address
Reserved
PG
CR0
CR1
CR2
CR3
0
31
11
12
The Page Directory Base Address locates the page directory for the page translation unit. Note that this address locates the page directory at any 4K boundary in the memory system because it is appended internally with a 000H.
The page directory contains 1024 directory entries of 4 bytes each. Each page directory entry addresses a page table that contains 1024 entries.
Thus, all put together, the page tables can totally access 1024 x 1024 entries or pages. If each page size is 4096 bytes, the entire 4GB addressing space is represented.
The Control Register Structure of the processor
PCD
PWT

## Slide 19
Paging Registers... Continued.
The linear address as it is generated by the software is broken into three sections that are used to access the page directory, page table entry and the page offset address.
The Page Directory is specified by the leftmost 10 bits. Note that 210 = 1024.
The Page Table Entry is specified by the next 10 bits. Again this is 210 = 1024.
The Page Offset is 12 bits which works out to 4096 which is the page size.
Each Page Directory represents a 4 MB region of memory.
Thus for linear address 00000000h to 002FFFFFh the first entry of the page directory is accessed.
Thus for linear address 00000000h to 00000FFFh, the first page directory and first page table entry is selected. This points to a 4K byte region. The offset now selects any single byte within this page table.
Because the act of repaging a 4K byte section of memory requires access to the page directory and a page table, both located in memory, Intel has incorporated a cache called the TLB or Translation Look Aside Buffer. In the 486 the cache holds the 32 most recent page translation addresses. If the same area of memory is accessed, the address is already present in the TLB and page directory and page tables is not required. speeding program execution. ( The Pentium have separate TLBs for each of their instruction and data caches.
Directory
Page Table
Offset
31
22
21
12
11
0